MAINTENANCE INSTRUCTIONS

OMNITECH EPOXY seamless floors will last for years by following simple cleaning procedures to maintain the surface.

Sweeping or dry mopping the floor as required to remove all loose dirt, litter, or foreign matter is highly recommended.

Floor areas subject to scratching by the tracking of sand or grit from outside sources must be swept frequently.

Periodically, as necessary, scrub the floor using a solution of a neutral detergent (such as “3M Spangle”) and water followed by a thorough rinsing with clear water.  Mopping with clear water only is not recommended, as the flooring will show water streaks when dry.

When the cleaning solution becomes dirty, discard it and mix a fresh detergent solution.  Hard to remove dirt, black marks, etc. should be rubbed gently with a scrubbing pad wetted with the detergent solution.

For scrubbing, a bristle, or nylon bristle brush is recommended.  If power scrubbing the non-slip surface, a nylon bristle scrubber head or non-abrasive pad such as 3M white, red or tan colored buffer pads should be used.

Never use an abrasive pad!

Promptly clean up all spillage of liquids, particularly oils or greases as these may penetrate and stain the floor.  Remove oils and greases with a mild detergent solution.  Immediately remove and neutralize all spillage of acids as such spillage may attack the flooring.