MAINTENANCE INSTRUCTIONS

SRS SEAMLESS FLOORING SYSTEM

SRS flooring systems will last for years and retain their sheen by following simple cleaning procedures to maintain the surface.

Sweeping or dry mopping the floor as required to remove all loose dirt, litter, or foreign matter is highly recommended. Floor areas subject to scratching by the tracking of sand or grit from outside sources must be swept frequently.

Periodically, as necessary, scrub the floor using a solution of neutral detergent and water followed by a thorough rinsing with clear water.  If the floor is being maintained by hand-mopping, care must be taken to ensure the mop water is changed often. When the cleaning solution becomes dirty, discard it and mix a fresh detergent solution.  Hard to remove dirt, black marks, etc. should be rubbed gently with a non-abrasive scrubbing pad wetted with the detergent solution.

SRS floors are normally finished with either a smooth or non-slip surface.  Smooth surfaces are readily mopped and need to be thoroughly dried before pedestrian traffic is permitted.  Non-slip surfaces should be power scrubbed using a nylon bristle scrubber head or non-abrasive pad such as “white”, “red”, or “tan” buffer pads.  Never use an abrasive pad!  After scrubbing is completed, rinse thoroughly with clear water.

Promptly clean up all spillage of liquids, particularly oils or greases as these may penetrate and stain the floor.  Remove oils and greases with a mild detergent solution.  Immediately remove and neutralize all spillage of acids as such spillage may attack the floor.

Do not use wax on SRS floors.  Wax will build upon the floor after repeated applications, trapping dirt and will require periodic stripping. Wax stripping can possibly damage floor surfaces.  These waxing and stripping procedures can be totally eliminated by following the above instructions.